## Slide 1: Snow depth monitoring using non-destructive imaging
Terrance Bariciak

## Slide 2: Introduction
Snow depth is an important climate variable
  Flood forecasting
  Hydroelectric reservoir management
  Habitat assessments
Methods
  Manual ruler
  Ultrasonic
  Structure for Motion (UAV)
  LIDAR

## Slide 3: Concept – Web Camera Imagery
MANUAL RULER APPROACH
AUTOMATED STAKE APPROACH

## Slide 4: Automated Stake Approach
INPUT IMAGE
OUTPUT RESULT
Filter out night images
Equalize
Register to reference template
Verify individual stakes
Determine intersection
Calculate snow depth
Green circles: snow point on stake
Yellow lines: used as secondary measurement of snow depth

## Slide 5: Reference Template
Template is required for snow depth measurement
  Registration
  Tensor (mm/pixel)
  Stake verification (presence)
    Minimum 2 red blobs
Selected by user
Can be snow/no snow
User defines stake and reference blob boundaries

## Slide 6: Filtering and Equalization

## Slide 7: Registration
Input image is registered to reference template
  Feature based (ORB)
  Intensity Based (ECC)
Simplifies stake verification and intersection

## Slide 8: Stake Verification
Stakes must be checked before the snow depth can be measured
  Using ROI from template, blob presence is confirmed
  Two or more blobs for valid stake
  Blob verification based off size of contour in HSV filtered image
Deep learning model is dynamically trained (yellow)

## Slide 9: Stake Verification
Invalid
Limitation of using HSV filter
Valid
Coordinates of blob will be used for tensor calculation and intersection
Valid (Deep Learning)
Blob recovered by neural network
Cannot be used for tensor calculation
Template coordinates are used for intersection

## Slide 10: Stake Verification

## Slide 11: Intersection
Three lines fitted to each stake
  Intensity signal along each line is processed
  Edge detection to improve accuracy
Distance from blob to snow intersection used as secondary measurement (yellow lines)

## Slide 12: Output
Excel spreadsheet
PDF image summary
PDF run summary
Snow depth graph (left)

## Slide 13: Intercomparison